## Slide 1: Gem5 Guide
Wang Hui
Sino-German Joint Software Institution
hui.wang@jsi.buaa.edu.cn

## Slide 2: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 3: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 4: What is Gem5
The combination of M5 and GEMS into a new simulator
  Google scholar statistics
    M5 (IEEE Micro, CAECW): 440 citations
    GEMS (CAN): 588 citations
  Best aspects of both glued together
    M5: CPU models, ISAs, I/O devices, infrastructure
    GEMS (essentially Ruby): cache coherence protocols, interconnect models

## Slide 5: Main Goals
Flexibility
  Multiple CPU models across the speed vs. accuracy spectrum
  Two execution modes: System-call Emulation & Full-system
  Two memory system models: Classic & Ruby
  Once you learn it, you can apply to a wide-range of investigations
Availability
  For both academic and corporate researchers
  No dependence on proprietary code
  BSD license
Collaboration
  Combined effort of many with different specialties
  Active community leveraging collaborative technologies

## Slide 6: Key Features
Pervasive object-oriented design
  Provides modularity, flexibility
  Significantly leverages inheritance e.g. SimObject
Python integration
  Powerful front-end interface
  Provides initialization, configuration, & simulation control
Domain-Specific Languages
  ISA DSL: defines ISA semantics
  Cache Coherence DSL (a.k.a.SLICC): defines coherence logic
Standard interfaces: Ports and MessageBuffers

## Slide 7: Capabilities
Execution modes: System-call Emulation (SE) & Full-System (FS)
ISAs: Alpha, ARM, MIPS, Power, SPARC, X86
CPU models: AtomicSimple, TimingSimple, InOrder, and O3
Cache coherence protocols: broadcast-based, directories, etc.
Interconnection networks: Simple & Garnet (Princeton, MIT)
Devices: NICs, IDE controller, etc.
Multiple systems: communicate over TCP/IP

## Slide 8: To us
Python and C++ with an event queue and a bunch of APIs

## Slide 9: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 10: Start with a simple example
suppose we want to run a hello world program
and suppose we have installed a number of packages and tools that gem5 depend on
  g++, python, scons, swig, zlib, m4, [mercurial]
  Ubuntu Server: sudo apt-get install mercurial scons swig python-dev g++ build-essential texinfo …
first we need to download the GEM5 Simulator source code
  Mercurial: hg clone http://repo.gem5.org/gem5 [-stable]
then we need to compile GEM5 Simulator

## Slide 11: Dependence
Tools
  GCC/G++ 3.4.6+
    Most frequently tested with 4.2-4.5
  Python 2.4+
  SCons 0.98.1+
    We generally test versions 0.98.5 and 1.2.0
    http://www.scons.org
  SWIG 1.3.31+
    http://www.swig.org
Other materials: (Full System Images, Cross Compiler, Benchmarks)
http://gem5.org/Download

## Slide 12: Start with a simple example
Compile Targets: build/<config>/<binary>
  config
    By convention, usually <isa>[_<coherence protocol>]
    ALPHA_MESI _CMP_directory
    Other ISAs: ARM, MIPS, POWER, SPARC, X86
    You can define your own config
  binary
    gem5.debug – debug build, symbols, tracing, assert
    gem5.opt – optimized build, symbols, tracing, assert
    gem5.fast – optimized build, no debugging, no symbols, no tracing, no assertions
    gem5.prof – gem5.fast + profiling support

## Slide 13: Start with a simple example
so let’s try this command to compile Gem5 Simulator:
and run the simulator:
Notes:
  If errors, first check the packages GEM5 depend on are installed
scons –j 2 build/ALPHA_MOESI_hammer/gem5.opt
./build/ALPHA_MOESI_hammer/gem5.opt configs/example/se.py –c test/test-progs/hello/bin/alpha/linux/hello

## Slide 14: Question on the simple example
what the output means?
what is configs/example/se.py? how it works?

## Slide 15: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 16: How se.py works?

## Slide 17: How se.py works?

## Slide 18: How se.py works?

## Slide 19: How se.py works?

## Slide 20: Summary on se.py --- Modes
gem5 has two fundamental modes
Full system (FS)
  For booting operating systems
  Models bare hardware, including devices
  Interrupts, exceptions, privileged instructions, fault handlers
Syscall emulation (SE)
  For running individual applications, or set of applications on MP/SMT
  Models user-visible ISA plus common system calls
  System calls emulated, typ. by calling host OS
  Simplified address translation model, no scheduling
Selected via compile-time option
  Vast majority of code is unchanged, though

## Slide 21: Summary on se.py --- Objects
Everything you care about is an object (C++/Python)
Derived from SimObject base class
  Common code for creation, configuration parameters, naming, checkpointing, etc.
Uniform method-based APIs for object types
  CPUs, caches, memory, etc.
  Plug-compatibility across implementations
    Functional vs. detailed CPU
    Conventional vs. indirect-index cache
Easy replication: cores, multiple systems, . . .

## Slide 22: Summary on se.py --- Events
Standard event queue timing model
  Global logical time in “ticks”
  No fixed relation to real time
    Normally picoseconds in our examples
Objects schedule their own events
  Flexibility for detail vs. performance trade-offs
E.g., a CPU typically schedules event at regular intervals
  Every cycle or every n picoseconds
  Won’t schedule self if stalled/idle
Now you knows how a Event Driven Simulator works --- the Simulator just fetch events from the EQ(Event Queue), all events generated by Objects and it produce new events and insert them into the EQ

## Slide 23: Summary on se.py --- Ports
Method for connecting MemObjects together
Each MemObject subclass has its own Port subclass(es)
  Specialized to forward packets to appropriate methods of MemObject subclass
Each pair of MemObjects is connected via a pair of Ports (“peers”)
Function pairs pass packets across ports
  sendTiming() on one port calls recvTiming() on peer
Result: class-specific handling with arbitrary connections and only a single virtual function call

## Slide 24: Summary on se.py --- Access Mode
Three access modes: Functional, Atomic, Timing
Selected by choosing function on initial Port:
  sendFunctional(), sendAtomic(), sendTiming()
Functional mode:
  Just “make it happen”
  Used for loading binaries, debugging, etc.
  Accesses happen instantaneously updating data everywhere in the hierarchy
  If devices contain queues of packets they must be scanned and updated as well
Atomic mode:
  Requests complete before sendAtomic() returns
  Models state changes (cache fills, coherence, etc.)
  Returns approx. latency w/o contention or queuing delay
  Used for fast simulation, fast forwarding, or warming caches
Timing mode:
  Models all timing/queuing in the memory system
  Split transaction
    sendTiming() just initiates send of request to target
    Target later calls sendTiming() to send response packet
Atomic and Timing accesses can not coexist in system

## Slide 25: Summary on se.py --- m5out/*
config.ini/config.json
  The simulated System
stats.txt
  Simulation Statistics
  you can generate statistic you needed by add some code, check GEM5 Tutorial for details
ruby.stats
  Ruby Statistics

## Slide 26: How to Debug?
Tracing
Using gdb to debug gem5
Python Debugging

## Slide 27: Tracing
printf() is a nice debugging tool
Keep good printfs for tracing
Lots of debug output is a very good thing
Example flags:
  Fetch, Decode, Ethernet, Exec, TLB, DMA, Bus, Cache, Loader, O3CPUAll, etc.
Print out all flags with --debug-help option
src/base/trace.*

## Slide 28: Enabling Tracing
Selecting flags:
  --debug-flags=Cache,Bus
  --debug-flags=Exec,-ExecTicks
Selecting destination:
  --trace-file=my_trace.out
  --trace-file=my_trace.out.gz
Selecting start:
  --trace-start=3000000
./build/ALPHA_MOESI_hammer/gem5.opt --debug-flags=MemoryAccess --trace-start=3000000 configs/example/se.py

## Slide 29: Adding Debuging
Print statement put in source code
  Encourage you to add ones to your models or contribute ones you find particularly useful
Macros remove them for gem5.fast or gem5.prof binaries
  So you must be using gem5.debug or gem5.opt to get any output
Adding an extra tracing statement:
  #include “debug/MyFlag.h”
  DPRINTF(MyFlag, “normal printf %snn”, “arguments”);
Adding a new debug flags (in a SConscript):
  DebugFlag(’MyFlag’)

## Slide 30: Using GDB with Gem5
Several gem5 functions designed to be called from GDB:
  schedBreakCycle() – also with --debug-break
  setDebugFlag()/clearDebugFlag()
  dumpDebugStatus()
  eventqDump()
  SimObject::find()
  takeCheckpoint()

## Slide 31: Using GDB with Gem5
wh@arch-node1:~/gem5-stable$ gdb --args ./build/ALPHA_SE/gem5.opt configs/example/se.py
GNU gdb (Ubuntu/Linaro 7.2-1ubuntu11) 7.2
...
(gdb) b main
Breakpoint 1 at 0x4087e0: file build/ALPHA_SE/sim/main.cc, line 41.
(gdb) run
Starting program: /home/wh/gem5-stable/build/ALPHA_SE/gem5.opt configs/example/se.py
[Thread debugging using libthread_db enabled]
Breakpoint 1, main (argc=2, argv=0x7fffffffe688) at build/ALPHA_SE/sim/main.cc:41
41 {
(gdb) call schedBreakCycle(1000000)
warn: need to stop all queues

## Slide 32: Using GDB with Gem5
(gdb) continue
Continuing.
gem5 Simulator System. http://gem5.org
gem5 is copyrighted software; use the --copyright option for details.
gem5 compiled Aug 29 2011 22:41:08
gem5 started Aug 29 2011 22:47:08
gem5 executing on arch-node1
command line: /home/wh/gem5-stable/build/ALPHA_SE/gem5.opt configs/example/se.py
Global frequency set at 1000000000000 ticks per second
0: system.remote_gdb.listener: listening for remote gdb #0 on port 7000
**** REAL SIMULATION ****
info: Entering event queue @ 0. Starting simulation...
info: Increasing stack size by one page.
Program received signal SIGTRAP, Trace/breakpoint trap.
0x00007ffff638dfe7 in kill () from /lib/x86_64-linux-gnu/libc.so.6
(gdb) p _curTick
$1 = 1000000

## Slide 33: Using GDB with Gem5
(gdb) print SimObject::find("system.cpu")
$2 = (SimObject *) 0x16aa980
(gdb) print (BaseCPU*)SimObject::find("system.cpu")
$3 = (BaseCPU *) 0x16aa980
(gdb) p $3->instCnt
$4 = 94699
(gdb) continue
Continuing.
Hello world!
hack: be nice to actually delete the event here
Exiting @ tick 3252000 because target called exit()
Program exited normally.

## Slide 34: Python Debugging
It is possible to drop into the python interpreter (-i flag)
  This currently happens after the script file is run
  If you want to do this before objects are instantiated, remove them from script
It is possible to drop into the python debugger (--pdb flag)
  Occurs just before your script is invoked
  Lets you use the debugger to debug your script code
Code that enables this stuff is in src/python/m5/main.py
  At the bottom of the main function
  Can copy the mechanism directly into your scripts, if in the wrong place for you needs
  import pdb
  pdb.set_trace()

## Slide 35: More
http://gem5.org/Debugging

## Slide 36: how to configure your architecture
http://gem5.org/Simulation_Scripts_Explained

## Slide 37: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 38: Cross Compiler
The first tool your need to prepared
check the Gem5 Status Matrix, ALPHA is the best supported architecture
I had compiled a alpha cross compiler, so your can copy it to use as your wish
How to use?
append this command to ~/.bashrc
export PATH=~/bin:~/alphaev67-unknown-linux-gnu/bin:$PATH

## Slide 39: Run your code under SE mode
compile your code with –static flag, Cross-Compiler
using config/example/se.py –c to run your_own_code
results:
alphaev67-unknown-linux-gnu-gcc –o sum sum.c –static –O2
./build/ALPHA_MOESI_hammer/gem5.opt configs/example/se.py –c /PATH/TO/sum

## Slide 40: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 41: Run SPLASH2 under SE mode
Get SPLASH2 Benchmark from http://gem5.org/Download
Run
./build/ALPHA_MOESI_hammer/gem5.opt configs/example/se.py -c benchmarks/splash2/codes/kernels/fft/FFT

## Slide 42: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 43: What is FS mode
load linux kernel
how to compile your kernel image?

## Slide 44: Full System related files
configs/common/SysPaths.py
  where is the disk image
configs/common/FSConfig.py
  pal, kernel
configs/common/Benchmarks.py
  disk image name
m5term
  cd util/term
  make
  sudo make install

## Slide 45: Run your code under FS mode
Preparation: put your code into the image
Run
sudo mount –o loop,offset=32256 linux-latest.img /mnt
sudo mkdir –p /mnt/benchmark/mybench
sudo cp sum /mnt/benchmark/mybench
sudo umount /mnt
scons build/ALPHA/gem5.opt
./build/ALPHA/gem5.opt configs/example/fs.py
m5term 3456
./sum

## Slide 46: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 47: Run SPLASH2 under FS mode
Preparation: put your code into the image
Run
sudo mount –o loop,offset=32256 linux-latest.img /mnt
sudo mkdir –p /mnt/benchmark/mybench
sudo cp FFT /mnt/benchmark/mybench
sudo umount /mnt
scons build/ALPHA/gem5.opt
./build/ALPHA/gem5.opt configs/example/fs.py
m5term 3456
./FFT -t

## Slide 48: Run SPLASH2 under FS mode
more convenient way?
Run
vi configs/common/Benchmarks.py
+ ‘fft’: [SysConfig(‘fft.rcS’, ‘512MB’)],
vi configs/boot/ffs.rcS
+ #!/bin/sh
+ cd benchmarks/mybench
+ echo “Running FFT now…”
+ ./FFT –t –p1
+ /sbin/m5 exit
scons build/ALPHA/gem5.opt
./build/ALPHA/gem5.opt configs/example/fs.py –n 1 –b fft
cat m5out/system.terminal

## Slide 49: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 50: Inside Gem5
Source Code Tree Organization

## Slide 51: Inside Gem5
Source Code Tree Organization
  configs: sample m5 scripts
  src/arch: architecture definition & ISA-specific components
  src/base: general data structures/facilities
  src/python: Python config code
  src/cpu, src/mem, src/dev: specific models
  src/sim: simulator base functionality
  system: platform specific code (palcode, firmware, bios, etc.) — packaged separately
  test: regression tests
  util: utility programs

## Slide 52: CPU Models Overview
Supported CPU Models
  AtomicSimpleCPU
  TimingSimpleCPU
  InOrderCPU
  O3CPU
CPU Model Internals
  Parameters
  Time Buffers
  Key Interfaces

## Slide 53: CPU Models Overview

## Slide 54: Supported CPU Models
Simple CPUs
  Models Single-Thread 1 CPI Machine
  Two Types: AtomicSimpleCPU and TimingSimpleCPU
  Common Uses:
    Fast, Functional Simulation: 2.9 million and 1.2 million instructions per second on the “twolf” benchmark
    Warming Up Caches
    Studies that do not require detailed CPU modeling
Detailed CPUs
  Parameterizable Pipeline Models w/SMT support
  Two Types: InOrderCPU and O3CPU
  “Execute in Execute”, detailed modeling
  Slower than SimpleCPUs: 200K instructions per second on the “twolf” benchmark
    Models the timing for each pipeline stage
    Forces both timing and execution of simulation to be accurate
    Important for Coherence, I/O, Multiprocessor Studies, etc.
src/cpu/*.hh,cc

## Slide 55: Inside Gem5---CPU Model

## Slide 56: Inside Gem5---CPU Model

## Slide 57: Inside Gem5---CPU Model

## Slide 58: Inside Gem5---CPU Model

## Slide 59: Inside Gem5---CPU Model

## Slide 60: Inside Gem5---Memory Model
General Memory System
  Ports
  Packets
  Requests
  Atomic/Timing/Functional accesses
Two memory system models
  Classic
  Ruby
Check http://gem5.org/General_Memory_System for details

## Slide 61: Ruby Memory Model
Flexible Memory System
  Rich configuration - Just run it
    Simulate combinations of caches, coherence, interconnect, etc...
  Rapid prototyping - Just create it
    Domain-Specific Language (SLICC) for coherence protocols
    Modular components
Detailed statistics
  e.g., Request size/type distribution, state transition frequencies, etc...
Detailed component simulation
  Network (fixed/flexible pipeline and simple)
  Caches (Pluggable replacement policies)
  Memory (DDR2)

## Slide 62: Ruby Memory Model
Can build many different memory systems
  CMPs, SMPs, SCMPs
  1/2/3 level caches
  Pt2Pt/Torus/Mesh Topologies
  MESI/MOESI coherence
Each components is individually configurable
  Build heterogeneous cache architectures (new)
  Adjust cache sizes, bandwidth, link latencies, etc...

## Slide 63: Ruby Memory Model
8 core CMP, 2-Level, MESI protocol, 32K L1s, 8MB 8-banked L2s, crossbar interconnect
  scons build/ALPHA_MOESI_hammer/gem5.opt
  ./build/ALPHA_MOESI_hammer/gem5.opt configs/example/ruby_fs.py -n 8 --l1i_size=32kB --l1d_size=32kB --l2_size=8MB --num-l2caches=8 --topology=Crossbar --timing
64 socket SMP, 2-Level on-chip Caches, MOESI protocol, 32K L1s, 8MB L2 per chip, mesh interconnect
  scons build/ALPHA_MOESI_hammer/gem5.opt
  ./build/ALPHA_MOESI_hammer/m5.opt configs/example/ruby_fs.py -n 64 --l1i_size=32kB --l1d_size=32kB --l2_size=512MB --num-l2caches=64 --topology=Mesh --timing

## Slide 64: Ruby Memory Model
Domain-Specific Language
  Syntatically similar to C/C++
  Like HDLs, constrains operations to be hardware-like (e.g., no loops)
Two generation targets
  C++ for simulation
    Coherence controller object
  HTML for documentation
    Table-driven specification (State x Event -> Actions & next state)

## Slide 65: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 66: Modify to meet your needs
All your need are provided
  Modify Python code
Miss some device your need
  Add C++ code
maybe need Modify the Linux Kernel

## Slide 67: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary

## Slide 68: Summary
The basics
Debugging
CPU model
Ruby memory system
How to use gem5
How gem5 works

## Slide 69: Summary

## Slide 70: Summary

## Slide 71: Further Read
http://gem5.org/Documentation
isca2011 Gem5 workshop slides
asplos2008 Gem5 tutorial slides

## Slide 72: Gem5 Guide Outline
What is Gem5?
Build & Run Gem5 Simulator
Gem5 Basics
Run your code under SE mode
Run SPLASH2 Benchmark under SE mode
Run your code under FS mode
Run SPLASH2 Benchmark under FS mode
Inside the Gem5
Modify to satisfy your needs
Summary